RT130 Demobilization SHEET  		     					Station:___________

Local Date/Time:___________________ GMT Date/Time:________________________

Field Team: ____________________________________________________________

GPS Location of Site: ____________________________________________________

## Equipment

DAS S/N:_______________

Clock S/N:_______________

Sensor S/N ______________	Sensor Type: 	________________

Get DAS initial Status:

DAS Status (Control ( Status)

Acq: 	Start On / Off

Events: ________			RAM:	________ of ________

Disk 1:	 ________ of ________	Disk 2:	________ of ________

Temp:	 ________			*Power: Input ______ Bkup chg: ______

Ch:	 ________			DS:	________

*If Power is Low, follow instructions at the end “IF POWER IS BAD…”.

Clock Status (Control ( Status (GPS)

Sec since LL:_______________ Phase Diff_____________ SV’s:_________

Mass Position Offsets (Control (Aux. Control (Aux Channel)

Ch 1:	__________________ V

Ch 2:   __________________ V

Ch 3:	__________________ V

Demob

1. Stop Acquisition (Control (Status (Stop Acq)

2. Get  RT130 parameters from the DAS

Work with Config  (From DAS (Edit (Verify experiment name: _______________

Get Sensor Serial Number:     	(Channels(Details(record sensor S/N above

3. Remove Disks  (wait for disk writing to finish)

Disk 1 S/N: _______ Size: _______	Orig.  Disk 2 S/N: _______ Size: _______

LABEL these DATA Disks – do not reuse them until data are downloaded and backed up

4. Lock sensor masses, wait 2 minutes

5. Check Mass Position Offsets (Control (Aux. Control (Aux Channel)

### If mass positions do not exceed modulo 8V, follow instructions at the end “IF POWER IS BAD…..”

Ch 1:	__________________ V

Ch 2:   __________________ V

Ch 3:	__________________ V

Make sure all plugs and connectors have been replaced.

# IF POWER IS BAD AND SENSOR IS CMG-3T

1. Connect fresh 12V battery to power port on breakout box

2. Lock masses using breakout box

3. Wait until mass positions exceed modulo 8V before disconnecting power

Comments: