SERVICE SHEET  		     					Station:___________

Local Date/Time:___________________ GMT Date/Time:________________________

Field Team: ____________________________________________________________

GPS Location of Site: ____________________________________________________

## Equipment

DAS S/N:_______________

Clock S/N:_______________

If tetlemetered: Modem S/N:_______________	Modem IP:________________

(Do the next step within the “Service” and look for sensor information in the parameter set from Clie below):

Sensor S/N ______________	Sensor Type: 	________________

Get DAS initial Status:

DAS Status (Control ( Status)

Acq: 	Start On / Off

Events: ________			RAM:	________ of ________

Disk 1:	 ________ of ________	Disk 2:	________ of ________

Temp:	 ________			*Power: Input ______ Bkup chg: ______

Ch:	 ________			DS:	________

*If Power is Low, follow instructions at the end “IF POWER IS BAD”; otherwise continue.

Clock Status (Control ( Status (GPS)

Sec since LL:_______________ Phase Diff_____________ SV’s:_________

Service

1. Stop Acquisition (Control (Status (Stop Acq)

2. Get  RT130 parameters from the DAS

Work with Config  (From DAS (Edit (Verify experiment name: _______________

Get Sensor Serial Number:     	(Channels(Details(record sensor S/N above

3. Swap Disks  (wait for disk writing to finish)

Orig.  Disk 1 S/N: _______ Size: _______	Orig.  Disk 2 S/N: _______ Size: _______

LABEL these DATA Disks – do not reuse them until data are downloaded and backed up

Swap Disk 1 S/N: _______ Size: _______	Swap Disk 2 S/N: _______ Size: _______

5. Clear RAM  (Control (RAM (Clear)

6. Reset System (Control (Reset) Note: this initializes the GPS

7. Format Flash Disk (Control (Format Disk ( Disk 1:______   Disk 2:______

8. Check Mass Position Offsets (Control (Aux. Control (Aux Channel)

### Mass position must be within +1.5V to –1.5V

Ch 1:	__________________ V

Ch 2:   __________________ V

Ch 3:	__________________ V

9. Monitor/Tap Test (Control (Monitor (Stream 1)

Ch 1:______		Ch 2: ______		Ch 3: ______

10. Check Clock Status (Control (Status (GPS)

Sec since LL:	_________________ *Note clock MUST lock before starting acquisition

Phase Diff ___________________ us (should be a small number)

SV’s: _____________

11. If telemetered : Check communications (Control (Net)

IP :         192.168.33.2			Line down: 	Toss

Mask : 	   255.255.255.0			Toss after: 	70 min

RTPD :	   129.138.26.198 (at PASSCAL)	E Control:	ON

Gateway:192.168.33.1

Communications OK: 	  Yes / No

12. Start Acquisition: (Control (Status (Start Acq)

Start time:	______________________________________

13. Verify RAM Increasing (Control (Status (Update)					Yes / No

14. Force RAM Dump to Disk – pull Disk 2  (Control (RAM (Dump)

Verify RAM decreases                     Yes / No

AND  Disk 1 increases         Yes / No    (Control (Status  (Update)

Replace Disk 2

*NOTE  Verify Disk 1 is (Current) and should be a non-zero value. (See below #17)

Disk 2 must be zero  (formatted and ready for data after Disk 1 is full)

15. Check Disk Setup (Control (Disk):

If telemetered:  Auto-wrap 	Yes

If stand-alone:  Auto-wrap 	No

16.  Write .CFG File to Disk (Control(Status(DAS LP/WP)

Tap the WRITE button to write the .cfg file to the disk.

Verify that the value of disk space used increases (Control (Status).

17. DAS status (Control (Status)

Acq: Start On / Off   - NOTE Acquisition MUST be ON to get data

Events:  ________			RAM:	 ________ of ________

*Disk 1:  ________ of ________	Disk 2: ________ of ________

Temp:   ________			Power: Input _______  Bkup chg:_____

Ch:        ________			DS: ________

Firmware Version________ (Control(Satus(Versions)

18. If telemetered: Communications status

(Control (Status (Net (Ethernet (RTP)

Connected	Yes / No

Server IP: 	___________________

Make sure all plugs and connections have been replaced.

# IF POWER IS BAD

POWER: Check Power ONLY IF the station has Power Problems

NOTE: The following tests should be performed with the solar panels in full sun. Check solar panel is clean.

1. Disconnect the solar panel.

2. Test output of the batteries (12.5 – 13 Volts DC

WARNING: DO NOT test the current of the battery)

3. Test the voltage out of the power box to the DAS from pin A+ to C-. (Same as battery voltage measured above).

! Make sure the polarity is correct

4. Test the solar panel output (18 Volts DC)

7. Connect the solar panels to power box

8. Test the voltage at the battery terminals (Greater than the battery voltage measured above).

Comments: